## Slide 1: Detector Parameters
Marco Sirianni - ESA

## Slide 2: JWST Detector Technologies
MID IR Detectors
Near IR Detectors
Technology: HgCdTe
Manufacturer: Teledyne
Size: 2048x2048 pixels
Operating Temp: ~40 K
Technology: Si:As
Manufacturer: Raytheon
Size: 1024x1024 pixels
Operating Temp: ~7 K
MIRI 3 (1 SCA) 5-28 mm
Each detector is called Sensor Chip Assembly (SCA)
The Focal Plane Array (FPA) of a given instrument can have one or
more SCAs
NIRCAM 2 FPAs (1 SCAs) 0.6-2.3 mm
NIRCAM 2 FPAs (4 SCAs) 2.4-5.3 mm
NIRSpec 1 FPA (2 SCAs) 0.6-5.3 mm
NIRISS 1 FPA (1 SCA) 0.6-5.3 mm

## Slide 3: MULTIACCUM - Non Destructive Readout
Signal
idle
reset
Non destructive
reads during
integration
Time
1
2
3
12
Hybrid technology allows to monitor
charges as they accumulate in each pixel
without erasing them
Fit to the slope provide the count rate
Several benefits of MULTIACCUM readout:
Multiple reads average down the read noise
History of the integration is maintained
Increase dynamic range
Signal
Time
Cosmic
ray hit
Signal
Time
1
2
3
12
Saturation

## Slide 4: Detector Concepts - Frame
The charge in each pixel is sampled with a regular cadence
All JWST detectors generally use 4 different outputs to simultaneously read four different areas of the detector.
FULL Frame
Subarrays are used to reduce the Frame Time
to observe brighter objects.
Full Frame Times:
NIRCAM & NIRISS 10.7 sec
NIRSpec 10.7 – 14.4 sec
MIRI 2.7 - 23.9 sec
The time needed to scan all the pixels in the selected array is the Frame Time
The entire array is
read out pixel by pixel
only a selected portion
of the detector is read out
SUBARRAY
NOTE: In APT AND ETC Full Frame is selected as SUBARRAY=FULL
Different instruments offer different subarrays (size, positions, use).
APT and ETC show only the subarrays offered in each observing mode (template).

## Slide 5
Each Read (Frame) can be save as a slice of a 3D data Cube
Detector Concepts - 3D CUBE
Signal
idle
reset
Non destructive
reads during
integration
Time
1
2
3
12
Time
1
2
12
When all reads are saved the readout pattern is called -RAPID
e.g. NRS-RAPID, NIS-RAPID etc
For MIRI all reads are always saved

## Slide 6
Detector Concepts - GROUPS
Getting all the reads in the ramp is the optimal situation, but it is not always feasible due to data volume limitations
Solution #1 - Average reads on board
Signal
idle
reset
Time
1
2
3
12
Time
1
10
11
4
9
1
2
2
3
3
Groups of reads
can be averaged
on board
N_FRAMES = Number of frames averaged in each group
Only the averaged
groups are sent to ground
NIRCam | 1, 2, 4, 8
NIRISS | 1, 4
NIRSpec | 1, 4, 5
MIRI | 1

## Slide 7
Detector Concepts - NSKIP (NIRCAM ONLY)
Solution #2 - Discarding some reads
Only a reduced number
ff groups are sent to
the ground
Signal
idle
reset
Non destructive
reads during
integration
Time
1
2
3
12
Time
1
2
12
11
10
11
10
3
Signal
idle
reset
Time
1
2
3
12
Time
1
2
12
11
10
11
10
3
Reads not
saved- “Skipped”
Readout Patterns
are a combination
of averaged frames
NFRAMES
and skipped frames
NSKIP

## Slide 8: Detector Concept - NSAMPLE - MIRI ONLY
MIRI always uses NFRAME=1 and NSKIP=0
But it offers two readout patterns:
FAST MODE: each pixel is sampled once before moving to the next one
NSAMPLE=1
Frame Time = 2.7 sec
Default mode for Imaging
SLOW MODE: each pixels is sampled multiple times to reduce read noise
NSAMPLE = 9
Frame time = 23.9 sec
Default mode for MRS

## Slide 9: Detector Concept - IRS2 - NIRSpec ONLY
Most NIRSpec observations are detector limited -> most stringent noise requirement
NASA/GSFC group analyzed noise properties of NIRSpec detector system and developed a new low noise readout scheme for NIRSpec Full Frame exposures.
“High level” recipe to reduce noise and noise correlation:
Send more reference pixels “to the ground” for post processing
Read reference pixels more frequently
Improved Reference
Sampling and Subtraction
Traditional
IRS2
Frame Time 10.7s
Frame Time 14.6s
Traditional
IRS2
Raw data
format
Processed dark
exposure

## Slide 10: READOUT PATTERN
The combination of NSAMPLE, NFRAMES, and NSKIP
defines the READOUT PATTERN used in one INTEGRATION
SI | READOUT PATTERN | NSAMPLE | NFRAMES | NSKIP
NIRISS | NIS-RAPID NIS | 1 1 | 1 4 | 0 0
NIRCam | RAPID | 1 | 1 | 0
 | BRIGHT1 BRIGHT2 | 1 1 | 1 2 | 1 0
 | SHALLOW2 SHALLOW4 | 1 1 | 2 4 | 3 1
 | MEDIUM2 MEDIUM8 | 1 1 | 2 8 | 8 2
 | DEEP2 DEEP8 | 1 1 | 2 8 | 18 12
NIRSpec | NRS-RAPID NRS | 1 1 | 1 4 | 0 0
 | NRSIRS2-RAPID NRSIRS2 | 1 1 | 1 5 | 0 0
MIRI | SLOW FAST | 9 1 | 0 0 | 0 0

## Slide 11: Integrations and Exposure
One exposure can have multiple identical integrations
Signal
idle
reset
Time
reset
reset
Integration #1
Integration #2
Integration #3
idle
Exposure
Multiple integrations reduce overheads
READOUT PATTERN
-RAPID

## Slide 12: NESTED Concept
FRAME #1 [ FRAME #2, FRAME #3, FRAME #4 …]
GROUP #1 [GROUP #2, GROUP #3, GROUP #4 …]
INTEGRATION #1 [INTEGRATION#2, INTEGRATION #3 …]
EXPOSURE #1 [EXPOSURE #2, EXPOSURE #3 …]
THE USER CAN SELECT :
FRAME TYPE (FULL OR SUBARRAY) - > SETS THE MINUM INTEGRATION TIME
READOUT TYPE -> SETS THE NUMBER OF FRAMES PER GROUP
NUBMER OF GROUPS - > SETS HOW LONG THE INTEGRATION WILL BE
NUMBER OF INTEGRATIONS
NUMBER OF EXPOSURES (e.g. NUMBER OF DITHERS)

## Slide 13: ASTRONOMER PROPOSAL TOOL (APT)
Once the instrument and the observing mode (TEMPLATE) are selected
only he available SUBARRAYS and READOUT PATTERNS can be selected in pull down menus
The user can adjust the NUMBER of GROUPS per integration
And the number of INTEGRATIONS per exposure
The selected combination will be repeated at each dither position
to produce the total number of integrations and total exposure time

## Slide 14: Exposure Time Calculator (ETC)
under the DETECTOR SETUP tab, user can select the available
READOUT PATTERN and SUBARRAY
Once the instrument and the observing mode (TEMPLATE) are selected,
Example : NIRCAM Imaging
The configuration for the ETC calculation is then completed with:
Number of GROUPS PER INTEGRATION
Number of INTEGRATIONS PER EXPOSURE
Number of EXPOSURES

## Slide 15: Detector Readout modes and patterns - JDOX Links
MIRI - https://jwst-docs.stsci.edu/display/JTI/MIRI+Detector+Readout+Overview
NIRSpec - https://jwst-docs.stsci.edu/display/JTI/NIRSpec+Detector+Readout+Modes+and+Patterns
NIRCam - https://jwst-docs.stsci.edu/display/JTI/NIRCam+Detector+Readout+Patterns
NIRISS - https://jwst-docs.stsci.edu/display/JTI/NIRISS+Detector+Readout+Patterns
Best practice JDOX pages provide useful hints and tradeoff discussion